## Slide 1: Lecture 3: Introduction to Flip-Flops and Finite State Machines
To watch lecture video click link below
Lecture 3a video
To view slides, continue to next slide

## Slide 2: Lecture 3: Introduction to Flip-Flops and Finite State Machines
Credit for un-cited Figures used in this Lecture:
Null and Lobur, The Essentials of Computer Organization and Architecture, 2e

## Slide 3: Lecture 3a: Introduction to Flip-Flops
picture credit: eroswholesale.com

## Slide 4: Overview
Digital Logic
  Combinational Circuits
  Sequential Circuits
Combinational Circuits (A Quick Review)
Sequential Circuits
  Clocks
  Flip-Flops
  Finite State Machines (Lecture 3b)

## Slide 5: Combinational Circuits: A Quick Review
Figure credit: unknown source.

## Slide 6: Commonly Used Gates

## Slide 7: Multiplexor
Note: Our textbook uses the 3rd notation.
Input: 2n
Output: 1
Control: n bits
Example: 4 x 1 Mux

## Slide 8: Decoder
Input: n bits
Output: 2n bits (only 1 bit is 1 all other bits 0)

## Slide 9: Sequential Circuits
A sequential circuit defines its output as a function of both its current input and its previous inputs.
  The output depends on past inputs!
  (Compare: combinational circuits only depend on current inputs.)
  Also called storage elements (i.e. a sequential circuit has memory!)

## Slide 10: Clocks
Clock Frequency or clock rate/speed: the number of cycles per second, e.g. 1MHz, 4GHz

## Slide 11: Flip-Flops
A circuit that is allowed to change state whenever the clock signal triggers
Latch vs. Flip-Flops
  Latch: level triggered
  Flip-Flops: edge triggered
  Note: here we do not distinguish Latch and Flip-Flops. We use Flip-Flop as a general term.

## Slide 12: SR Flip-Flop (SR: Set/Reset)

## Slide 13: Truth Table
S | R | Q(t+1)
0 | 0 | Q(t) (no change)
0 | 1 | 0 (reset to 0)
1 | 0 | 1 (set to 1)
1 | 1 | undefined
S | R | Q(t) | Q(t+1)
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | undefined
1 | 1 | 1 | undefined
Characteristic table or partial truth table
Complete Truth Table

## Slide 14: SR Flip-Flop: Summary

## Slide 15: JK Flip-flop
To ensure situations such as undefined states in SR flip-flop will never arises
Named after Texas Instruments engineer Jack Kilby

## Slide 16: JK Flip-Flop: Summary

## Slide 17: D Flip-flop (D: Data)
D | Q(t+1)
0 | 0
1 | 1
Character Table

## Slide 18: D flip-flop as modified SR flip-flop

## Slide 19: Application of D Flip-Flops: Registers
A Register File built with D Flip-Flops. Left: Register read circuits; Right: Register write circuits.

## Slide 20: Summary and To-Do List
Differences between combinational circuits and sequential circuits;
  Question: how to distinguish combinational and sequential circuits?
The principles and operations (character or truth tables) of three types of flip-flops;
Registers: a popular usage of flip-flops.
To Do
  zyBook 8.7 & 8.8