## Slide 1: Lecture 4b : Number Representations
To watch lecture video click link below
Lecture 4b video
Correction: in video Lecture 3b should be Lecture 4b
To view slides, continue to next slide

## Slide 2: Lecture 4b : Number Representations
Machines speak binary!

## Slide 3: Binary Representation
Bits are just 0s and 1s (no inherent meaning)
  conventions define relationship between bits and numbers/instructions
Numbers
  Binary numbers (base 2) 0000 0001 0010 0011 0100 0101 0110 0111
    Decimal range of a 32-bit binary number: 0 .. 2n-1
  two’s complement representation
    To represent both positive & negative numbers
Instructions
  Represented by binary numbers too
Expected background: familiar with binary numbers

## Slide 4: Hex Numbers
Hex (short for hexadecimal): Base 16
Hex numbers: 0-9, A-F
Examples
010111112 5F16
Hex: better readability/writability
A prefix 0x commonly used as to indicate it’s a hex number
0x5F 5F16
Hex | Binary
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001
A | 1010
B | 1011
C | 1100
D | 1101
E | 1110
F | 1111

## Slide 5: Binary -> Hex
Convert a 32-bit binary number to a 8-digit hex number:
  00100000111110100101110000111110 split to 4 digits in a group
  0010 0000 1111 1010 0101 1100 0011 1110 convert 4 bits to a hex
  2 0 F A 5 C 3 E
So we have 0x20FA5C3E

## Slide 6: Hex -> Binary
Convert a 4-digit hex to binary:
0x3A25 convert each digit to binary
  0011 1010 0010 0101 combine, that’s the result.
Practice:
convert 0x20FA5C3E to binary
In many cases, for convenience, we will use hex to represent binary.

## Slide 7: Signed Number Representations
Sign Magnitude One's Complement Two's Complement 000 = +0 000 = +0 000 = +0 001 = +1 001 = +1 001 = +1 010 = +2 010 = +2 010 = +2 011 = +3 011 = +3 011 = +3 100 = -0 100 = -3 100 = -4 101 = -1 101 = -2 101 = -3 110 = -2 110 = -1 110 = -2 111 = -3 111 = -0 111 = -1
Issues: balance, number of zeros, ease of operations
Which one is best?
  Most commonly used: 2’s complement
Sharing question:
why 2’s complement?

## Slide 8: Two’s complement representation: Review
Two’s complement representations
5 => 0101 -5 => 1011
  How to represent a negative number in 2’s complement?
    Invert all bits, then add 1.
Special note
Here 2’s complement representation of number doesn’t mean to negating (or taking 2’s complement operation) of that number.
Therefore, 2’s complement representation of 5 is 0101 (do not to convert 5 to -5!)

## Slide 9: Sign Extension of Two’s Complement Numbers
Converting n-bit numbers to more than n bits:
  For example: 4-bit representation of 5 and -5 are as follows:
  5: 0101 -5: 1011
  To extend to 8-bit representation
  copy the most significant bit (the sign bit) into the other bits 0101 -> 0000 0101 1011 -> 1111 1011
  This is called "sign extension"
Usage in MIPS (Module 6)
e.g. addi instruction’s 16-bit immediate gets converted to 32 bits for arithmetic operations.
Warning: don’t just add 0s in front
e.g. 1011 -> 00001010
After extension, 8-bit now actually represents 10 (not -5!)

## Slide 10: MIPS Number Representation
32 bit signed numbers (in 2’s complement representation) 0000 0000 0000 0000 0000 0000 0000 0000two = 0ten 0000 0000 0000 0000 0000 0000 0000 0001two = + 1ten 0000 0000 0000 0000 0000 0000 0000 0010two = + 2ten ... 0111 1111 1111 1111 1111 1111 1111 1110two = + 2,147,483,646ten 0111 1111 1111 1111 1111 1111 1111 1111two = + 2,147,483,647ten 1000 0000 0000 0000 0000 0000 0000 0000two = – 2,147,483,648ten 1000 0000 0000 0000 0000 0000 0000 0001two = – 2,147,483,647ten 1000 0000 0000 0000 0000 0000 0000 0010two = – 2,147,483,646ten ... 1111 1111 1111 1111 1111 1111 1111 1101two = – 3ten 1111 1111 1111 1111 1111 1111 1111 1110two = – 2ten 1111 1111 1111 1111 1111 1111 1111 1111two = – 1ten
Special values: 0, largest positive number, most negative number, -1
Note: remember the binary representation of these special values.

## Slide 11: Addition & Subtraction
Just like in grade school (carry/borrow 1s) 0101 0111 0110 + 0001 - 0110 - 0101 0110 0001 0001
Two's complement operations easy
  subtraction using addition of negative numbers 0110–0101=>0110+(-0101)=>0110+1011 => 1111 (-1)
  (the extra carryout is not needed, this is not an overflow case.)
Overflow (result too large for finite computer word):
  e.g., adding two n-bit numbers does not yield an n-bit number 0111 + 0001 This is an overflow case.
  1000 In case of overflow, not necessary to have a carryout.

## Slide 12: Illustration: Binary Addition with Carries
Note: we will not cover details of 2’s complement operations (add, sub). What we need to know are the overflow situation of these operations (see next slide).

## Slide 13: Overflow Detection in Additions
a | b | a + b | Overflow?
Positive (start with 0) | Positive | Positive | No
Positive | Positive | Negative | Yes
Negative (start with 1) | Negative | Negative | No
Negative | Negative | Positive | Yes
Positive | Negative | Don’t care | Never
Negative | Positive | Don’t care | Never
Note: we ignore cases for subtraction as subtraction of 2’s complement is done via addition.

## Slide 14: Meaning of bits
Bits don’t have inherent meanings.
For example, a memory location contains the following 32-bit sequence
  10001101100110000000000000010100
  Thinking questions: Under MIPS architecture, what does this bit sequence represent?

## Slide 15: Meaning of bits
Bits don’t have inherent meanings.
For example, a memory location contains the following 32-bit sequence
  10001101100110000000000000010100
  Thinking questions: Under MIPS architecture, what does this bit sequence represent?
  Hint: it could represent a binary number in 2’s complement; or it could represent a MIPS instruction (next Lecture), or it could represent a floating-point number (Module 5), …

## Slide 16: Summary
What we covered
  Number representations (whole numbers)
    binary, hexadecimal
    unsigned, two’s complement
  Integer addition/subtraction, overflow