## Slide 1: Lecture 4c : MIPS Instruction Set
To watch lecture video click link below
Lecture 4c video
Correction: in video Lecture 3c should be Lecture 4c
To view slides, continue to next slide

## Slide 2: Lecture 4c : MIPS Instruction Set

## Slide 3: Binary Representation of MIPS Instructions
Why binary representation?
  Memory location can only store 0s and 1s;
  Instructions are stored in the memory;
  Therefore, binary representation of instructions.
How to represent MIPS instructions in binary?
  Three types of instructions
    R type (for instructions of operands in registers)
    I type (for instructions with immediate data)
    J type (for jump instruction with memory address)
How to: that’s an important ISA design issue.

## Slide 4: MIPS Instruction Set: Reference Data
This is the most important resource for MIPS instruction set.
  Attached in Module 3
  It’s commonly called Green Sheet
    in hardcopy of the book, printed on green paper.
Table 1: Basic Instruction Format (on lower left corner.)

## Slide 5: R-type instructions
Format (fits one 32-bit word)
  opcode rs rt rd shamt funct
  6 bits 5 5 5 5 6
    opcode: operations of the instruction (6 bits)
    rs: register source 1 (5 bits)
    rt: register source 2 (5 bits)
    rd: register destination (5 bits) Note: rd (destination) at the last.
    shamt: shift amount (5 bits)
    funct: function code (6 bits)
Instructions
  add, sub, and, or, …,

## Slide 6: R-type Format: Explanation
Opcode (6 bits)
  ISA designers decided to use 6 bits for opcode;
    Detailed explanation omitted here.
  That means we’re able to represent 26 different operations
    e.g. opcode could be 000000, up to 111111
Register numbers are 5 bits (why? – thinking questions)
  Hint: review machine organization, how many (int) registers MIPS has?
Shamt (shift amount) 5 bits
  Not used in our case, so let these be 00000
Funct (function code) 6 bits
  These are 6 extra bits available in R-type;
  What can we use these bits?
    Which of the above fields would like to have more bits?

## Slide 7: Funct Code
This is the special design of MIPS
  MIPS would like to use these extra bits to support more operations (i.e. as an extension to opcode).
The Design:
  When opcode is 000000, it represents a group of arithmetic and logic operations
    R-type instructions thus refer to Arithmetic/Logic instructions
  Specific operations are designated by funct code, e.g.
  add: opcode is 000000, funct code is 2016 (i.e. 3210)
  or: opcode is 000000, funct code is 2516 (i.e. 3710)
  (see highlighted text in next slide)

## Slide 9: Converting R-type Instructions to Binary
Example Add R8, R17, R19
Step 1: Check MIPS Reference Data (Green Sheet)
  Under row Add, column Format: we found R
Step 2: Bring up R-format
Step 3: Fill in add R8, R17, R19 info to R-format fields
Opcode (6 bits) | Rs (5 bits) | Rt (5 bits) | Rd (5 bits) | Shamt (6 bits) | Funct (6 bits)
add | 17 | 19 | 8 | 0 | funct
Notes: (1) register order: destination register #, R8 move to last, i.e. Rd;
(2) Shamt: it’s always 0

## Slide 10: Converting R-type to Binary(cont)
Step 4: Find opcode and funct from MIPS Reference Data (The last column: 0/20hex
Step 5: Put opcode and funct to the fields
Step 6: Convert to binary according to the bits in each field
Step 7: Final result 000000 10001 10011 01000 00000 100000
Could be written as:
0000 0010 0011 0011 0100 0000 0010 0000
0 | 17 | 19 | 8 | 0 | 20hex
Note: to fit 20hex into 6 bits, use 2 bits for 2 (10) and 4 bits for 0 (0000), thus, 20hex -> 00 1000
000000 | 10001 | 10011 | 01000 | 00000 | 100000

## Slide 11: Practice
Note: In zyBook, register conventions such as $s0, $t0 are used. Convert these registers to direct register numbers first.
Let’s try for And R9, R15, R17
Hints:
  Please note the difference between opcode and funct.
  It’s AND instruction, not ADD instruction.

## Slide 12: Practice
The bit pattern below represents a MIPS instruction, what does it represent?
0000 0001 1111 0001 0100 1000 0010 0100
(hint: similar strategy as previously but in reverse direction.)

## Slide 13: I-type Instruction Format
Format
  Opcode rs rt address
  (6 bits) (5) (5) (16)
Instructions
  beq (opcode: 4), bne (opcode: 5), …
  For simplicity, we provide these two instructions in the following format where the 16-bit offset is given in hex format.
  beq R16, R17, 0x0008
  lw (opcode: 23hex or 3510), sw (opcode: 2bhex or 4310), …
  lw R15, 0x0008 (R16)
  sw R15, 0x0004(R16)
  addi, andi, ori, …

## Slide 14: Converting beq/bne to Binary
Instruction: beq R16, R17, 0x0008
Step 1: MIPS reference -> Format for beq is I.
Step 2: Bring up I format
Step 3: Fill up I format with instruction details
Note: MIPS swaps Rs, Rt => explanation omitted. In our exercise, either 16, 17 order or 17, 16 order okay.
Step 4: Convert to binary
Final result:
0001 0010 0011 0000 0000 0000 0000 1000
Opcode (6) | Rs (5) | Rt (5) | Imm (16)
Beq opcode: 4 | 17 | 16 | 0x0008
000100 | 10001 | 10000 | 0000 0000 0000 1000

## Slide 15: lw and sw Instructions
lw: load a word from memory
e.g. lw R8, 0x0020(R18)
Per discussion in Lecture 3a, the memory address of data is calculated as:
addr <- Reg[R18] + SignExt(0x0020)
Then, we load the data from memory to R8, i.e.
Reg[R8] <- Mem[addr] #read from memory
sw: store a word to memory
e.g. sw R8, 0x0020(R18)
Memory address calculation: same as lw
To store data: Mem[addr] <- Reg[R8] #write to memory

## Slide 16: Converting lw/sw to Binary
Instruction: lw R8, 0x0020(R16)
Step 1: MIPS reference -> Format for lw/sw is I.
Step 2: Bring up I format
Step 3: Fill up I format with instruction details
Note: in this example R16 is Rs, R8 is the Rd for lw and Rt for sw.
Step 4: Convert to binary
Final result for lw:
1000 1110 0000 1000 0000 0000 0010 0000
(for sw, the opcode is 0x2b, i.e. 101011, all other parts are the same. )
Opcode (6) | Rs (5) | Rt /Rd (5) | Imm (16)
lw opcode: 0x23 | 16 | 8 | 0x0020
100011 | 10000 | 01000 | 0000 0000 0010 0000

## Slide 17: J-type Instruction Format
Format:
  Opcode address
  (6 bits) (26 bits)
Instruction: J addr
Conversion of J instruction to binary omitted.

## Slide 18: Practice
Same MIPS instructions
  Lw R24, 0x0014(R12)
  Addi R24, R12, -4
  #Note: First, convert -4 to 16-bit 2’s complement, then follow the conversion procedure we stated, with reference to the “Green Sheet” you should be able to convert this one.
  Beq R24, R12, 4

## Slide 19: Practice
Given the instruction bit patterns, what instruction (specially) does each represent?
  100011 01100 11000 0000000000010100
  001000 01100 11000 1111111111111100
  000100 01100 11000 0000000000000100

## Slide 20: Summary
MIPS instructions
    R-type
      Opcode: 000000
      For a group of arithmetic and logic operations
    I-type
      With an immediate in instructions
      Focused on beq, bne, lw, sw instructions
      Additional instructions such as addi, andi, ori can be learned in similar way
    J-type
      Details omitted