## Slide 1: Lecture 4d: Addressing Modes
To watch lecture video click link below
Lecture 4d video
Correction: in video Lecture 3d should be Lecture 4d
To view slides, continue to next slide

## Slide 2: Lecture 4d: Addressing Modes

## Slide 3: MIPS Addressing Modes
MIPS Features
  Load-store (register-register) architecture
  Simple addressing mode
Five Addressing Modes
  Immediate addressing (e.g. addi)
  Register addressing (e.g. add)
  Base addressing (e.g. lw, sw)
  PC-relative addressing (e.g. beq)
  Pseudo-direct addressing (e.g. j)

## Slide 4
Figure 2.10.1
Illustration of Addressing Modes
Errata: ”address” should be “offset”

## Slide 5: Immediate Addressing
Immediate Addressing
  Data/Operand stored in the instruction, immediately available.
Example: addi R8, R16, 5
I-type instruction
The sum of Register 16 content and (sign-extended) immediate value 5 will be stored in R8
Here the 2nd operand (i.e. value 5) is stored in the instruction directly as immediate value => Immediate addressing for this operand.
000100
(opcode)
10000
(R16)
01000
(R8)
0000 0000 0000 0101
(value 5 in 16 bits)

## Slide 6: Register Addressing
Register Addressing
  Data/Operand stored in the register
  Register number is available in the instruction
Example
  add R8, R16, R17
R16
R17
000000
(opcode)
10000
(R16)
10001
(R17)
01000
(R8)
00000
(shamt)
100000
(funct)
32-bit value

## Slide 7: Base Addressing
Base Addressing
  Data/Operand stored in the memory
  Memory address is calculated by adding the content of a base register with an offset value
    The # of base register is available in the instruction
    The offset value is also available in the instruction
Example
lw R8, 0x0020 (R16)
i.e. $t0 = A[8], with A’s starting address in R16

## Slide 8: Base Addressing: Illustration
SignExt
+
R16’s content (32-bit)
0x 0000 0020 (32-bit)
lw
10000
(R16)
01000
(R8)
0000 0000 0010 0000
(0x0020 16-bit)
Memory

## Slide 9: PC-Relative Addressing
PC-relative addressing
  The next PC is relative to the current PC
    i.e. Next PC is PC + offset
    Data to be fetched: the next instruction stored in memory
Example
beq R16, R17, 0x0020 #offset: 0x0020, i.e. 32
Assume current PC: FFFF0000
offset*: 0x0020
Next PC: FFFF0020
*in case word offset is used, we need to convert to byte offset (i.e. offset is 32 words, which meant 32*4 = 128 bytes.) We will discuss Module 6.

## Slide 10: Pseudo-Direct Addressing
Pseudo-Direct Addressing
  For the J (jump) instruction, the next PC address should be in the instruction.
  Example: J Exit
    Here Exit is the next instruction’s PC.
    However, PC has 32 bits, can’t fit into the whole instruction, so partial address is used.
    Details omitted here.
Opcode (6 bits) | Address (26 bits)

## Slide 11: RISC Architecture
RISC: Reduced Instruction Set Computer
Developed in 1980s
Prior to RISC, CISC Architecture popular
  CISC: Complex Instruction Set Architecture
MIPS is a RISC architecture
Features of RISC
  Simple instruction format (e.g. in MIPS only R, I, and J)
  Only loads/stores reference memory (load-store architecture)
  Highly pipelined (to be discussed in Module 7)
  Instructions executed by hardware (reflected in Module 6 design)
  Few instructions and modes (simplicity)
  Complexity in the compiler
  Multiple register sets
    MIPS: integer R0, … R31, floating point F0, .., F31

## Slide 12: Summary
Addressing modes
RISC architecture (introduction)