## Slide 1: Lecture 5b: Integer Multiplication
To watch lecture video click link below
Lecture 5b video
To view slides, continue to next slide

## Slide 2: Lecture 5b: Integer Multiplication
Figure credit: pinterest.com

## Slide 3: Multiplication
More complicated than addition
  accomplished via shifting and addition
Here we study unsigned number multiplication
  algorithms discussed here don’t apply to 2’s compliment numbers
Negative numbers: convert and multiply
  multiple absolute values first, then decide the sign;
  there are better techniques for signed number multiplication, but we won’t have time to look at them
Study approach
  We will present two versions of multiplication hardware diagrams
  Be able to trace them to understand the principle of operations
  Focused on version 1, though version 2 is a better/optimized one.

## Slide 4: Multiplication Example (binary numbers)
1 0 0 1
x 1 1 0 1
1 0 0 1
0 0 0 0
1 0 0 1
1 0 0 1
1 1 1 0 1 0 1

## Slide 5: Multiplication Algorithm – Version 1

## Slide 6: Multiplication Hardware Diagram: Version 1

## Slide 7: Tracing (0010 x 0011)
zyBook Figure 3.3.3

## Slide 8: Homework #3 – Problem 1
Tracing Version 1 hardware diagram for
1001 x 1101
Note: the product will be an 8-bit number.
Pause, work on the problem!

## Slide 9: Version 1 Problem
Required hardware
  Product: 64-bit Register
  ALU: 64-bit
  Multiplicand: 64-bit (because of shift)
Problem:
  Cost too much (64-bit ALU, 64-bit registers)
Version 2: Sharing product with multiplier
  Optimal for hardware resource

## Slide 10: Multiplication: Version 2

## Slide 11: Version 2 Features
Features
  Multiplicand never change/move
  When product extends space, multiplier comes with extra space
  Add multiplicand to high 32-bit of the product and then shift the product 1bit right every time
Use minimum hardware resources
  32-bit ALU, 1 32-bit and 1 64-bit Registers
  Hardware easily implementable
Details omitted.

## Slide 12: Signed Number Multiplication
Method 1
    MSB as sign bit (0 for positive, 1 for negative)
    Deciding the sign bit of the product
      0 x 0 -- > 0, 1 x 0 -- > 1, 0 x 1 -- > 1, 1 x 1 -- > 0
      xor operation
    Unsigned multiplication for the remaining n-1 bits.
Method 2
  In unsigned multiplication algorithms, the shifting steps would need to extend the sign of the product for signed numbers (details omitted)

## Slide 13: MIPS Assembly for Mult & Div
Instruction format, e.g.
mult Rs, Rt #$hi, $lo = product of $Rs * $Rt
  (Note: here $Rs, $Rt refer to 32-bit content of registers Rs, Rt respectively.)
Storing result
  No need to list destination registers
  Results automatically stored in two special registers, $hi and $lo
$hi
$lo
$hi: left half of product register
$lo: right half of product register

## Slide 14: $hi and $lo registers
Accessing results
  Use two additional instructions
  e.g. mfhi $t1 #move from $hi to $t1
  mflo $t2 #move from $lo to $t2
  #hi, lo are two special registers, can only be accessed by mfhi/mflo
$hi and $lo for division
  div Rs, Rt #$lo=$Rs/$Rt, $hi=$Rs mod $Rt
  Though we didn’t talk about integer division, it also uses $hi and $lo, similar to multiplication, but with quotient in $lo and remainder in $hi.

## Slide 15: Summary
Unsigned number multiplications
  Version 1 focused
  Version 2 optimized in hardware resources
Signed number multiplications
  Sign treatment
MIPS instructions for multiplication
  Use of $hi and $lo
Thinking Questions
Assume multiplicand 32-bit, multiplier also in 32-bit, product 64-bit.
  Possible to have overflow in unsigned number multiplications?
  Possible to have overflow in signed number multiplications? Assume we multiply two 31-bit unsigned numbers first, then determine the sign.