## Slide 1: Lecture 5d: FP Addition
To watch lecture video click link below
Lecture 5d video
To view slides, continue to next slide

## Slide 2: Lecture 5d: Floating Point Addition

## Slide 3: How to add two FP numbers?
Let’s review how we do in decimals
Example: 9.986 * 103 + 7.836 * 102
Step 1: Align exponents (shift the number with smaller exponent)
9.986 * 103 + 0.7836 * 103
Step 2: Add fractions
9.986 + 0.7836 = 10.7696
(i.e. 10.7696 * 103)
Step 3: Normalize the sum
10.7696 * 103 => 1.07696 * 104
Step 4: Rounding
1.07696 * 104 => 1.0770 * 104
Why shift the number with smaller exponent, not the one with larger exponent?

## Slide 4: Floating Point Addition
Addition of FP in binary is the same as that of decimal values
  Here we assume adding two positive FP numbers.
Algorithm idea
  Step 1: shift the fraction of the one with smaller exponent (Exponent compare, shift/alignment)
  Step 2: add the fractions
  Step 3: normalize the sum
  Step 4: round the sum
Example
Flowchart
  In this class, we will ignore the discussion of Exception, as well as the need for “re-normalization” caused by “rounding”.

## Slide 5: FP Addition in Binary
Same as in decimal
Example
1.11011 * 22 + 1.01011 * 2-1
Step 1: Exponent compare, shift/alignment
  1.11011 * 22 + 0.00101011 * 22
Step 2: add
1.11011 * 22 + 0.00101011 * 22 = 10.000000011 * 22
Step 3: normalize
10.000000011 * 22 => 1.0000000011* 23
Step 4: round
1.0000000011* 23 => 1.00000 * 23

## Slide 6: FP Addition of IEEE 754 numbers
0 10000001 1101 1000 0000 0000 0000 000 (1.11011 * 22)
+ 0 01111110 0101 1000 0000 0000 0000 000 (1.01011 * 2-1)
Step 1: Exponent compare, shift/alignment
  10000001 - 01111110 = 310
  2nd number shift right 3 times (note: must recover hidden 1)
  1 01011000000000000000000 => 000101011000000000000000000
Step 2: add (with hidden 1 recovered)
111011000 0000 0000 0000 000 + 000101011 000000000000000000
=> 10 00000011 000000000000000000
Step 3: normalize
10 0000001100 … 0 => 1 0000001100…00
exponent: 10000001 + 1 => 10000010
Step 4: round
1 00000011 000000000000000000 => 1 0000 0011 0000 0000 0000 000
Final result: 0 10000010 0000 0011 0000 0000 0000 000

## Slide 7: FP Addition Algorithm: Flowchart
zyBook Figure 3.5.2
ignored
ignored

## Slide 8: How we implement FP addition algorithm?
Task
  Build a hardware unit that implements FP addition
  FP numbers represented in IEEE 754 single precision
Hardware diagram
  Next slide (zyBook Figure 3.5.3)
  What we should know from the diagram?
    Input and output format
    How it performs Step 1 and step 2 of addition?
      Will ignore step 3 and step 4
  Details about the hardware diagram omitted.

## Slide 9: FP Addition Hardware Diagram
zyBook Figure 3.5.3

## Slide 10: FP Subtraction
The hardware diagram (with minor modification) can actually perform FP subtraction
  In the diagram the sign of two input data is not connected to the output’s sign.
  We can use a – b => a + (-b) if we deal with signs properly.
  Details omitted here.

## Slide 11: Overflow and Underflow
During the addition, overflow and underflow may occur.
Could you give an example, i.e. give two FP numbers a and b such that a + b would have an overflow?
  Overflow: a = ? b = ? (note: many possible a’s and b’s.)
  (Review Overflow/Underflow definition in Lecture 5c. More to discuss at Lecture 5e FP Multiplication.)

## Slide 12: Floating Point Complexities
Accuracy can be a big problem
  May not be associative
    x+(y+z)= -1.5*1038+(1.5*1038+1.0)= -1.5*1038+1.5*1038=0
    (x+y)+z=(-1.5*1038+1.5*1038)+1.0=0+1.0=1.0
  Limited accuracy
    IEEE 754 keeps two extra bits, guard and round during addition
Other complexities
    positive divided by zero yields “infinity”
    zero divide by zero yields “not a number”
Standard
  Implementing the standard can be tricky
  Not using the standard can be even worse
Pitfalls
  see zyBook 3.9 for description of 80x86 and Pentium bug!
    Optional, not for credit.