## Slide 1: Lecture 5e: FP Multiplication
To watch lecture video click link below
Lecture 5e video
To view slides, continue to next slide

## Slide 2: Lecture 5e: Floating Point Multiplication

## Slide 3: How to multiply two FP numbers?
Let’s review how we do in decimals
Example: +9.986 * 103 multiplies -7.836 * 102
Step 1: Determine the sign
s = s1 xor s2
Step 2: Add exponent
3 + 2 = 5
Step 3: Multiply fractions
9.986 * 7.836 = 78.250296
Step 4: Normalize the sum
78.250296 * 105 => 7.8250296 * 106
Step 5: Rounding
7.8250296 * 106 => 7.8250 * 106 -7.8250 * 106 (final result)
s1 (sign 1) | s2 (sign 2) | s (result sign) s= s1 xor s2
0 (+) | 0 (+) | 0 (+)
0 (+) | 1 (-) | 1 (-)
1 (-) | 0 (+) | 1 (-)
1 (-) | 1 (-) | 0 (+)

## Slide 4: Multiply two FP binary numbers
-1.11011 * 22 multiply - 1.01011 * 2-1
Step 1: Determine the sign
s = s1 xor s2 = 1 xor 1 = 0 (negative * negative -> positive)
Step 2: Add exponent
2 + (-1) = 1
Step 3: Multiply fractions
1.11011 * 1.01011 = 10.0111101001
Step 4: Normalize the sum
10.0111101001 * 21 => 1.00111101001 * 22
Step 5: Rounding
1.00111101001 * 22 => 1.01000 * 22
Final result: +1.01000 * 22

## Slide 5: Multiply two IEEE 754 FP numbers
0 10000001 1101 1000 0000 0000 0000 000 (1.11011 * 22)
* 1 01111110 0101 1000 0000 0000 0000 000 (-1.01011 * 2-1)
Step 1: Determine the sign
s = s1 xor s2 = 0 xor 1 = 1 (positive * negative -> negative)
Step 2: Add exponent subtract bias (thinking question: why subtract bias?)
10000001 + 01111110 – 01111111 = 1000 0000
Step 3: Multiply fractions (recover hidden 1)
1.110110…0 * 1.010110...0 = 10.011110100100…0
Step 4: Normalize the sum
10.01111010010…0 => 1.001111010010…0
Exponent add 1: 1000 0000 => 1000 0001
Step 5: Rounding
1.00111101001000000000000 (hide the leftmost 1 in result)
Final result: 1 1000 0001 00111101001000000000000

## Slide 6: Floating-point Multiplication Algorithm
Easier than FP addition
Steps:
  Determine the sign of the product
  Add exponents (e1 + e2 – bias)
  Multiply fractions (recover the hidden 1’s and use unsigned multiplication)
  Normalize the product
  Rounding
  Final result (remove hidden 1)

## Slide 7: FP Multiplication Algorithm
zyBook Figure 3.5.4

## Slide 8: Implementing FP Multiplication Algorithm
s1
e1
s2
s
e2
e
f1
f2
f

## Slide 9: Step 1: determine sign
s1
e1
s2
s
e2
e
f1
f2
f
xor

## Slide 10: Step 2: Add Exponents
s1
e1
s2
s
e2
e
f1
f2
f
xor
e1+e2-127
Use two adders/ALUs for e1+e2-127 (details omitted )

## Slide 11: Step 3: Multiple Fractions
s1
e1
s2
s
e2
e
f1
f2
f
xor
e1+e2-127
1.f1 * 1.f2
1.f
Recover hidden 1. Use unsigned multiplication unit as discussed in Lecture 5b.

## Slide 12: Rest of Steps
Step 4: Normalization
Step 5: Rounding
(step 4 and step 5 details omitted)
Finally packing result:
Sign (already determined)
Exponent (may be affected by normalization)
Fraction (after rounding, hide the leftmost “1”)

## Slide 13: MIPS FP Instructions
FP numbers, once loaded from memory, are stored in FP registers
32 FP registers available in MIPS
  F0, F1, … F31
  Each Fi is 32-bit so can store a single-precision FP number
  A double precision FP number is stored in a pair of FP registers
    Pairs: F0 & F1, F2 & F3, … F30 & F31
    Only even numbered FP registers could be named in storing double
MIPS instructions for FP operations
add.s add.d sub.s sub.d mul.s mul.d div.s div.d
#.s for single; .d for double precision
add.s F15, F13, F12
add.d F16, F14, F12 #only even numbered registers can be used.

## Slide 14: Overflow/Underflow, Accuracy/Precision
Thinking Questions
  Could you give two FP numbers a, and b such that a multiplies b will yield an overflow?
  Same as above, but this time a multiplies b will yield an underflow.
  After the step 3 (before normalization and rounding) how many bits of precision we have in the product?
  Which operation (addition or multiplication) affects the accuracy more?

## Slide 15: Lecture 5 Summary
Computer arithmetic is constrained by limited precision
  Limited bits (32 bits, 64 bits, …)
Bit patterns have no inherent meaning but standards exist
  two’s complement
  IEEE 754 floating point
Computer instructions determine “meaning” of the bit patterns
  How can you tell the meaning of a seq. of 32 0s and 1s?
  MIPS integer and FP operations, e.g. add, add.s, add.d
Implementation of operations
  Hardware diagrams and their “abstractions”
    ALU, unsigned Multiplication unit
    FP adder, FP multiplier
  Functionality of these hardware modules