## Slide 1: Lecture 6b: Building Datapath for MIPS Instructions
To watch lecture video click link below
Lecture 6b video
To view slides, continue to next slide

## Slide 2: Lecture 6b: Building Datapath for MIPS Instructions

## Slide 3: The Processor: Datapath & Control
We will Implement the following MIPS instruction set:
  arithmetic-logical instructions: add, sub, and, or
  memory-reference instructions: lw, sw
  control flow instructions: beq
Generic Implementation:
  use the program counter (PC) to supply instruction address
  get the instruction from memory
  read registers
  use the instruction to decide exactly what to do

## Slide 4: Implementation Steps
Two common steps
  Step1: Instruction fetch
    Send the Program Counter (PC) to Instruction Memory (IM) to fetch the instruction;
    Increase the PC by 4 – get ready for the next instruction.
      Each instruction occupies one word, i.e. 4 bytes.
      In case of branch instruction, PC will be further updated.
  Step 2: Read operands
    Read two registers using fields of the instruction to select the registers to read. For lw instruction, we need to read only one register (no harm to read 2nd one, just don’t use it).
Remaining steps
  Depends on specific actions required by the instruction

## Slide 5: More on Implementation Steps
Arithmetic-Logical Instructions: and, or, add, sub
  Use ALU for opcode/function code execution
  Write the data from ALU back to register
  e.g. add R15, R14, R13
Memory –Reference Instructions: lw, sw
  Use ALU for calculating effective address
  Access memory for storing a word or loading a word
  e.g. sw R15, 0x0100(R20)
Branch Instructions: beq
  Use ALU for comparison
  Change the next PC based on the comparison
  e.g. beq R15, R0, 0x0100

## Slide 6: How to Build up a Datapath
General methods
  For each instruction,
    Analyze the detailed actions of instruction execution step by step
    Build up the datapath for each step
  For all the instructions
    The datapath for a processor should be able to execute any of the above instruction at a time;
    Datapaths for different instructions share common functional units
    Combine paths together using multiplexors

## Slide 7: Step 1: Instruction Fetch (IF)
Actions
  Fetch the instruction (read instruction memory with PC as address)
    Instruction <= IM[PC] #here we borrowed programming notations to describe hardware actions
  Increment PC (PC <= PC+4)
Building blocks
  Instruction Memory (IM)
  Program Counter (PC)
  Adder
    To increment the PC

## Slide 8: Building Blocks for IF

## Slide 9: First Step: Linking Together
Instruction <= IM[PC]
PC<=PC+4
Strategy for linking:
Just simply connect each functional unit’s input and output, i.e. PC connects to IM’s Read address.

## Slide 10: R-type Instructions
Remaining steps
  Read two registers
  ReadData1 <= Registers[rs]
  ReadData2 <= Registers[rt]
  Use ALU to compute the result
    ALUResult <= ReadData1 op ReadData2
    op: addition for add instruction, AND for and instruction, …
  Write back the result to registers
    Register[rd] <= ALUResult
Components involved: Registers and ALU

## Slide 11: Building Blocks for R-type Instructions

## Slide 12: R-type Instructions: Linking Together
rs
rt
rd

## Slide 13: rs, rt, rd
From Step 1, we have read out from IM 32-bit instruction, and which is R-type (by assumption)
Recall R-type instruction format (reference: green sheet.)
A 32-bit instruction, leftmost is bit 31, rightmost is bit 0
Opcode (6 bits) uses bits 31 to 26, rs (5 bits) uses bits 25 to 21, …
Therefore, we could refer
rs  Instruction[25:21]
rt  Instruction[20:16]
rd  Instruction[15:11]
Opcode (31:26) | rs (25:21) | rt (20:16) | rd (15:11) | Shamt (10:6) | Funct (5:0)

## Slide 14: R-type: Connecting with Step 1
rs
rt
rd
The green bar illustrates the 32-bit instruction from IM (not stored, just 32-bit data lines) with bits 26:21 connecting to Read reg 1; bits 20:16 to Read reg 2, and bits 15:11 to Write reg.

## Slide 15: Load (lw) Instruction
Actions
  Read two registers (2nd useless, so ignored)
  ReadData1 <= Registers [rs]
  Use ALU to compute memory address
    Addr <= ReadData1 + SE(offset)
      Offset: Instruction[15:0]
      sign extension needed to convert offset (16-bit) to 32-bit before addition
  Value from DM writes back to register
    ReadData <= DM[Addr] #note: ReadData from DM
    Reg[rd] = ReadData
Components involved:: Registers, ALU, DM, and SE

## Slide 16: Linking Together
rs
rd
Instr[15:0]
Opcode(31:26) rs(25:21) rd(20:16) offset(15:0)
I-type
lw

## Slide 17: Store (sw) Instruction
Actions
  Read two Registers
    ReadData1 <= Registers[rs]
    ReadData2 <= Registers[rt]
  Use ALU to compute memory address (same as lw)
    Addr <= ReadData1 + SE(offset)
  Write to DM
    DM[Addr] <= ReadData2 #note: ReadData2 from Registers
Components involved
  Registers, ALU, DM, and SE (sign extend)
    Same as lw

## Slide 18: Linking Together
Opcode(31:26) rs(25:21) rt(20:16) offset(15:0)
I-type
sw
rs
rt
Instr[15:0]
Here two lines not connected, just cross over.

## Slide 19: Branch Equal (beq) Instruction
Actions
  Read two Registers
    ReadData1 <= Registers[rs] ReadData2 <= Registers[rt]
  Use ALU to compute compare two values
    ReadData1 – ReadData2 == 0?
    (note: ALU performs subtraction, and Zero output will indicate the result isZero or not.)
  Update PC
    if (isZero) PC <= PC + SE(offset) #note: condition check will be done by control unit. No to worry at this moment.
Components involved: Registers, ALU, SE, adder
    An additional adder for for PC + SE(offset)

## Slide 20: Datapath for beq

## Slide 21: Why we need a ”shift left 2” unit?
byte address vs. word address
    beq R8, R9, Label
    and …
    or …
    j Exit
    Label: sub R24, R20, R22
What should be the value for Label in instruction?
  It’s an offset between beq and sub instructions
  Remember after we fetch beq, PC already incremented by 4
  So if branch taken, PC needs to point to sub instruction by adding additional 12 bytes (i.e. skipping 3 instructions)
  MIPS put 3 (3 words) for Label in the instruction, but the actually PC needs to increase by 3 * 4 = 12 bytes
    Shift left 2  multiply by 4
Note: Some assembly may put R8, R9 order in instruction differently. Don’t care here as no affect to result.
beq: I-type
beq opcode
Label
R9
R8

## Slide 22: Instruction Implementation: Summary
Instructions implemented
    Add, sub, and, or, slt, lw, sw and beq
Actions and hardware components
  Fetch instructions and increment PC (PC, IM, adder)
  Read two operands (registers)
  ALU
    R-type: ALU operations as defined by the function code
    Lw & sw: add offset with base register value for calculating effective address
    Beq: compare two registers to see if equal
  DM (lw & sw) or update PC (beq)
  Write back register (R-type instructions and lw)

## Slide 23: Special Notes to the Datapath
R-type instructions (and, or, add, sub) share the exact same datapath.
  The only difference among these instructions is the ALU operation, i.e. overall instruction execution for these four instruction is the same, but ALU will perform and, or, add, sub respectively (see Lecture 6d ALU control.)
It’s no harm to read the second register in case of lw as the value of the second register will not be used.
In case of beq, PC increment will not be performed by the ALU. In addition, a special adder is used to increment PC.

## Slide 24: Thinking Question
MIPS has an I-type addi instruction. It works as follows:
addi R14, R12, 0x0014
Meaning: Regs[14] <= Regs[12] + SE (0x0014)
Could you build up a datapath for the addi instruction?
opcode (6 bits) | 01100 (R12) (5 bits) | 01110 (R14) (5 bits) | 0000 0000 0001 0100 (16-bit immediate)

## Slide 25: Summary
Implemented each instruction individually
Next lecture: putting together into one datapath
What you should understand
  Actions in each step of execution
  Hardware unit to perform each action
  Linking units together to form the datapath