## Slide 1: Lecture 6e: Main Control Design
To watch lecture video click link below
Lecture 6e video
To view slides, continue to next slide

## Slide 2: Lecture 6e: Main Control Design

## Slide 3: Control Signals on Datapath

## Slide 4: Concurrent Behavior of Hardware Units
For any instruction execution, all hardware units are functioning.
However, the results of some units are blocked by some controls.
For example, if the instruction in execution is lw, the result of adder (connected to shift left 2 unit) is blocked by PCSrc (for lw, PCSrc is 0).

## Slide 5: What Control Signals needed for the datapath?
RegWrite: controls the write action to the registers
MemRead and MemWrite: control the read and write actions to the DM
Each MUX needs a control signal as selector
  It selects one and only one input to go through;
  It could be x (don’t care) if output not used.
  We give each a meaningful name, e.g.
    RegDst to select the rd (3rd in instruction for R-type, 2nd for lw)
    ALUSrc to select ALU’s 2nd operands (i.e. ReadData2 or immediate.)
ALUOp (2-bit) as we discussed in ALU control
No control signals needed for IM, PC as we explained in Lecture 6a

## Slide 6: Main Control Unit

## Slide 7: Abstraction of Main Control Unit
The input to the main control:
6-bit opcode
(from opcode we know which instruction it is, for that instruction we know which datapath it takes, thus we know all the control signals for that instruction.)
Output of the main control:
all the signals for the datapath
(ALUOp is a 2-bit signal while others all 1-bit signal.)
Input to main control
Outputs of main control

## Slide 8: Determining Control Values
Selecting the operations to perform (ALU, read/write, etc.)
Controlling the flow of data (multiplexor inputs)
Information comes from the 32 bits of the instruction
Example: add R8, R17, R18 Instruction Format: R 000000 10001 10010 01000 00000 100000 op rs rt rd shamt funct
ALUOp: 10 (from Lecture 6d) RegWrite: 1 (write back to rd)
MemRead: 0 MemWrite: 0 (no memory action)
Branch: 0 (not a beq instruction)
note: PCSrc = Brand and Zero (i.e. jump only if branch instruction and equal.)
Other signals: determined by datapath

## Slide 9: Controlling MUX for R-type Instructions
RegDst: 1
ALUSrc: 0
MemtoReg: 0

## Slide 10: Strategies in Designing the Main Control
Background
  How ALUOp generated?
  How MUXs controlled?
  When and how to set memory read and write signals?
  When and how to set registers read signal?
Control signals
  RegDst, RegWrite, ALUSrc, ALUOp, MemWrite, MemRead, MemToReg, PCSrc
  From the instruction’s opcode, all the above signals but one (PCSrc) can be generated
  PCSrc needs the result of ALU comparison (zero) and a control signal Branch control signal: PCSrc=zero and Branch

## Slide 11: Strategies: Role of the Control Signals
RegDst
  For R-type instructions, such as add R12, R15, R16, Instruction[15-11], i.e. the 3rd register number (i.e. rd) should be used to write the register file. So, RegDst should be set to 1.
  For lw, such as lw R12, 0x0100(R15), Instruction[20-16], i.e. the 2nd register number should be used to write the register file. So, RegDst should be set to 0.
ALUSrc
  For R-type and beq instructions, the 2nd register read should be fed to ALU, so ALUSrc should be set to 0.
  For lw and sw, the offset with sign extension should be fed to ALU, so ALUSrc should be set to 1.
Similar analysis for other signals

## Slide 12: Strategies: Instructions => Control Signal Values
Tracing each instruction’s datapath => get the control values
We’ve given R-type instruction example
We’ll give one more example: lw
Practice: do the same for sw and beq
Once figure out controls values for each instruction => construct a truth table

## Slide 13: Control Values for lw
From datapath:
RegDst: 0 ALUSrc: 1
MemtoReg: 1
From instruction itself:
Branch: 0, ALUOp: 00
From datapath or instruction:
RegWrite: 1, MemRead: 1
MemWrite: 0

## Slide 14: Opcodes and the Control Signals: Truth Table
Note: from the highlighted datapath, if a MUX not marked, then the control signal could be X (don’t care).

## Slide 15: Truth Table of Control Unit
Note: you get this table by filling in the opcode value at the table shown in previous slide, then turn the table 90o.

## Slide 16: Implementation of Control Signals
Note: implementation details not further discussed in this class.

## Slide 17: Summary: The Simple Control Structure
All of the logic is combinational
Need to wait for everything to settle down, and the right thing to be done
  ALU might not produce “right answer” right away
  use write signals along with clock to determine when to write
Cycle time determined by length of the longest path
  CPI = 1 (but a long cycle so clock rate must be very slow.)
  Not good performance
Improvement: small but multiple cycles, and pipelined!

## Slide 18: Practice
So far we have created a Simple Scheme that includes datapath and control for the implementation of a subset of MIPS instruction.
Now, we’d include the following instructions on the datapath, what changes, if any, you’d make to the datapath as well as control unit(s)? Add each instruction independently.
addi
ori
bne