## Slide 1: Lecture 7: Pipelining
To watch lecture video click link below
Lecture 7a video
To view slides, continue to next slide

## Slide 2: Lecture 7: Pipelining
This lecture covers the pipelined operation of the processor

## Slide 3: Lecture 7a: Pipeline Basics
Outline
  Principle of pipelined operations
  Pipeline performance

## Slide 4: Single Cycle Implementation Performance Issues
Longest delay determines clock cycle time
  Critical path: load instruction
  Instruction memory  register file  ALU  data memory  register file
Not feasible to vary cycles for different instructions
Violates design principle
  Principle: Making the common case fast
We will improve performance by pipelining

## Slide 5: Pipelining Concepts: Its Natural!
Laundry Example
  Ann, Brian, Cathy, Dave each have one load of clothes to wash, dry, fold, and store
  Washer takes 30 minutes
  Dryer takes 30 minutes
  “Folder” takes 30 minutes
  “Store” takes 30 minutes
A
B
C
D

## Slide 6: Laundry analogy for pipelining
Above: sequential execution
Left: Pipelined execution

## Slide 7: Sequential Laundry vs. Pipelined Laundry
Pipelined Laundry: Start Work ASAP
  Start work as soon as the resource is available
  Overlapping execution
Performance: Parallelism improves performance
  Speedup = Tseq = sequential execution time Tpiped = pipelined execution time
  4 loads: Tseq = 2 hours each * 4 = 8 hours; Tpiped = 3.5 hours total
  Speedup= 8/3.5 = 2.3
  Non-stop (n loads, when n is very large)
  Tseq = 2 * n (every job takes 2 hours, n jobs take 2n hours)
  Tpiped = 1.5 (start-up cost) + 0.5 * n (every 30 min one job done)
    Speedup = ≈ 4 (when n => = number of stages
    (total 4 stages in laundry example)

## Slide 8: Questions on Pipelining
Will pipeline help if only do 1 load?
What if
  Washer takes 30 minutes
  Dryer takes 40 minutes
  “Folder” takes 20 minutes
  “Store” takes 10 minutes
Note: A lot of special cases or complexities will not be discussed here. We first consider “ideal” pipeline and then, in next lecture introducing some critical “hazards” that must be resolved for pipelined execution.

## Slide 9: MIPS Pipeline
Five stages, one step per stage
  IF: Instruction fetch from memory
  ID: Instruction decode & register read
  EX: Execute operation or calculate address
  MEM: Access memory operand
  WB: Write result back to register

## Slide 10: 5-Stage MIPS Pipeline
Hardware for each stage
  IF
    Major unit: Instruction Memory (IM)
    Others: PC, adder
  ID - Register (Reg)
  EX- ALU
  MEM – Data Memory (DM)
  WB – Register (Reg)
Clock cycles
  Each stage uses one clock cycle
  Register access takes less time, so under edge triggered technology, at one cycle, we may use the 1st half cycle for write, the 2nd half cycle for read.
    Next lecture will explain why write at 1st half, read at 2nd half cycle.

## Slide 11: Multi-Cycle Pipeline Diagram
Graphical representation of pipelined execution
At each (small) cycle one instruction is launched for execution.

## Slide 12: Simplified Graphical Representation
Cycle | C1 | C2 | C3 | C4 | C5 | C6 | C7 | C8 | C9
lw | IM | Reg | ALU | DM | Reg |  |  |  | 
sub |  | IM | Reg | ALU | DM | Reg |  |  | 
add |  |  | IM | Reg | ALU | DM | Reg |  | 
lw |  |  |  | IM | Reg | ALU | DM | Reg | 
add |  |  |  |  | IM | Reg | ALU | DM | Reg
MIPS pipeline features:
All instructions go through 5 stages; even a stage not used (e.g. DM in sub, add not used) it still occupies a cycle.
In each cycle, no resource conflicts among instructions (e.g CC4 sub is using ALU, thus, no other instruction could use ALU.)
Reg may be used by two instructions at one cycle if one is reading and the other is writing. (write at 1st half cycle, read 2nd.)

## Slide 13: Multi-Cycle Pipeline Diagram Resource Usage
Reg: right half shaded => read; left half shaded => write
IM and DM: no shade => no memory action; shaded => read/write (please consider the half shaded as fully shaded. Detailed explanation omitted.)

## Slide 14: Pipeline Operation
Cycle-by-cycle flow of instructions through the pipelined datapath
  Use graphical representation to illustrate the instruction execution time chart
  Resource usage can also be illustrated
This is the ideal situation of pipelined execution
Many factors may complicate pipelines

## Slide 15: Pipeline Lessons
Pipelining doesn’t help latency of single task, it helps throughput of entire workload, i.e.
  Looking at each instruction individually, the execution time not improved;
  However, within the same amount of time, pipeline can execute more instructions than sequential;
  multiple tasks operating simultaneously.
Pipeline rate limited by slowest pipeline stage
  Every stage uses one cycle;
  Clock cycle time must fit the slowest pipeline stage.
Potential speedup = Number pipe stages
Unbalanced lengths of pipe stages reduces speedup
Time to “fill” pipeline or time to “drain” it reduces speedup
  Considered as start-up cost

## Slide 16: Practice
Assume an instruction sequence lw, add, sw, or, add, sw, lw is executed on pipeline ideally,
  create a pipeline diagram (simplified version okay) to illustrate the execution;
  what is ALU doing during cycle 4?
  what is DM doing during cycle 4?
  how many cycles does it take to execute this code?
  Ignore any pipeline overhead, what is the speedup compared with sequential execution?