## Slide 1: Lecture 8: Memory Hierarchy
To watch lecture video click link below
Lecture 8a video
To view slides, continue to next slide

## Slide 2: Lecture 8: Memory Hierarchy
This lecture covers the Memory Organization

## Slide 3: Memory Components
SRAM:
  value is stored on a pair of inverting gates
  very fast but takes up more space than DRAM (4 to 6 transistors)
DRAM:
  value is stored as a charge on capacitor (must be refreshed)
  very small but slower than SRAM (factor of 5 to 10)

## Slide 4: Memory Technology
Access time and Price
Ideal memory: users want large and fast memories!
  Access time of SRAM
  Capacity and cost/GB of disk

## Slide 5: Memory Hierarchy: Current Technology

## Slide 6: Lecture 8a: Basics of Cache
In this Module we will focus our discussions on cache. Lecture 8a on basics of cache and Lecture 8b on cache performance.

## Slide 7: Cache
Meaning
  A safe place for hiding or storing things – Webster’s Dictionary
  Level of the memory hierarchy between processor and main memory
Two issues:
  How do we know if a data item is in the cache?
  If it is, how do we find it?
Basic Terms
  block: minimum unit of data
  hit: data requested is in the upper level (i.e. in cache)
  miss: data requested is not in the upper level

## Slide 8: Principles of Locality -- design foundation for Cache
Temporal locality
  if an item is accessed, it will tend to be referenced again soon
    e.g. if x is accessed, x will likely be accessed soon so keep/put x in cache.
Spatial locality
  if an item is accessed, nearby items will tend to be referenced soon.
    e.g. if an instruction fetched, the instruction stored next to it will likely to be fetched. So put a block of consecutive instructions in cache likely will benefit.
    e.g. for (int i = 0; i< n; i++) sum += a[i];
  If a[i] is accessed, likely a[i+1] will be accessed next.
  A block of consecutive data in cache likely will benefit.

## Slide 9: A Simple, Direct Mapped Cache
Block size: one word
Direct mapped: many to one mapping
  A low level data can only be mapped to one location in cache (only one choice)
  Different low level data may be mapped to the same location
  Location determined by address
Cache address =
(memory address) mod (#Blocks in cache)
# of blocks: in power of 2
In this example:
Cache: 23 blocks
addr mod 23
 take last 3 bits in addr
e.g. 11001 maps to 001.
(assume memory address is word address)

## Slide 10: Practice
Assume we have a direct-mapped cache with 16 blocks, each block is one word.
Memory address is byte based. Assume memory address is 8-bit long.
What cache block address will each of the following memory addresses map to? (note: memory is byte-addressed.)
00111000, 11001100, 10111000
Can we map the following address to the cache? Why or why not?
00111010, 11001111

## Slide 11: Tags and Valid Bit
How do we know which particular block is currently stored in a cache location?
  Store block address as well as the data
    Actually, only need to store the high-order bits
    Lower bits of the address is the same as the cache address
  Tag: the high/left part of the memory address stored in the cache along with the cached data
What if there is no data in a location?
  Valid bit: 1 = present, 0 = not present
    Initially 0

## Slide 12: Cache Example
Cache organization: 8-blocks, 1 word/block, direct mapped
Initial state of the cache:
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 

## Slide 13: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Miss | 110
Access a word in cache
Miss, read from memory and then put it to cache, per temporal locality

## Slide 14: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
26 | 11 010 | Miss | 010
one more word
Miss, and update cache

## Slide 15: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Hit | 110
26 | 11 010 | Hit | 010
two more words
Hit, read from cache directly

## Slide 16: Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
16 | 10 000 | Miss | 000
3 | 00 011 | Miss | 011
16 | 10 000 | Hit | 000
more accesses
Updated cache content

## Slide 17: Implementation of Direct-mapped Cache
A 4KB cache
(each block is 1 word, so total 1K blocks)
Hit =1
if Valid=1 && tag==upper_addr
Data found in cache if hit == 1
32-bit memory address

## Slide 18: Hit and Miss
hit: data requested found in cache
  Data is sent from cache to processor datapath directly
  This makes it possible for the memory (IM/DM) read in 1 cycle
miss: data requested is not cache
  In case of cache miss, the pipeline will be stalled
  Read data from the memory (many more cycles)
  Put it in cache
    According to temporal locality, if a data is accessed, likely it will be used again soon
  Send to the processor datapath
  Cache miss penalty
    Much larger than pipeline hazard penalty
    For example: 10-20 cycles

## Slide 19: Summary
Memory hierarchy
  The fastest (also smallest due to cost) is closest to processor
  Larger (and cheaper) memory in lower level
  Caching, a strategy that
    views the memory as the largest one
    accesses via the fastest one first
Concepts of Cache
  Principle of locality
    Programs use a small part of the memory space frequently
  Direct-mapped cache principles and organization