## Slide 1: Lecture 8b: Cache Performance
To watch lecture video click link below
Lecture 8b video
To view slides, continue to next slide

## Slide 2: Lecture 8b: Cache Performance
Outline:
Cache overhead
Impact to CPI by cache miss penalty
Strategies for improving cache performance

## Slide 3: Implementation of Direct-mapped Cache
A 4KB cache
Cache overhead

## Slide 4: Cache Overhead
Cache size, i.e. data storage space the cache
  4KB (i.e. 1 K words) given
  Each block 1 word => total 1K blocks for cache
  For 1K (210 blocks) the cache address is 10 bits.
Total cache storage space: data storage + overhead
  Valid bit: 1 bit each row * 1K rows = 1K bits
  Tag: 20 bits each row * 1K rows = 20K bits
    Memory address 32 bits – 2 bits word offset – 10 bits cache address = 20 bits
  Overhead = 1K bits + 20K bits = 21K bits => 2.625 KB
  Data: 4KB
  Total cache: 4KB + 2.625 KB = 6.625 KB
Overhead % = = = 65.6%
Observation: for a 4KB cache, need additional 65.6% of storage to implement the cache – very high overhead!

## Slide 5: Practice: Calculating Cache Size
How many total storage needed to implement a directed-mapped cache with 64KB of data with one-word per block, assuming a 32-bit memory address?
Note: in previous example, word offset 2 bits meant that the last two bits of a word address always 00.
  Remember: memory are byte addressed and words are aligned so must start at an address of multiple of 4.

## Slide 6: Practice: Calculating Cache Size
How many total storage needed to implement a directed-mapped cache with 64KB of data with one-word per block, assuming a 32-bit memory address?
Answer
  64KB = 16K words = 214 words = 214 blocks
  Tag: 32 – 2 (word offset) – 14 bits (cache address) = 16 bits
  Overhead: 214 (blocks) * (1 + 16) bits = 17*214 bits = 17*24 Kbit
  = 34 KB
  Total cache size: 64KB (data) + 34KB (overhead) = 98 KB
  Cache overhead: = 53%
How to reduce cache overhead and improve hit rate?
  Hit rate = (higher hit rate => less miss penalty)

## Slide 7: A 64-KB Cache w/ 4-word Block
Larger block: take advantage of spatial locality

## Slide 8: Larger block size: reduced overhead
Cache (data) size
Overhead
From the illustration it is obvious that the overhead is much smaller relative to the data size.

## Slide 9: Larger block size: higher hit rate
Higher hit rate  lower miss rate
  Each miss carries a cache miss penalty
Why hit rate higher when block size is larger? Example:
  Given the memory address of an access sequence: 1, 2, 3, 4, 5, 6, 7, 8, …
  Assume cache block size is 4 words
    If block size is 1 word, all above access is miss.
    For block size of 4 words:
address | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
 | miss | hit | hit | hit | miss | hit | hit | hit
When the first is a miss, it reads a whole block (a block of 4 consecutive words from memory to cache, thus here the next 3 accesses are hit. – take advantage of spatial locality.

## Slide 10: Cache with multiple words in a block
Research found: Increase block size will reduce miss rate, but may increase miss penalty.
  The figure below shows when block size increases to 32 or 64 words, miss rate reduced.
  Miss penalty: in case of a miss, have to bring up a “larger” block, thus cost more, i.e. higher penalty.
Here we introduced the concepts and advantage of cache with multiple words per block, details (implementation and operation) omitted.

## Slide 11: Calculating Cache Performance
Assumption
  Instruction cache miss rate: 2%
  Data cache miss rate: 4% (freq. of load and store: 36%)
  Miss penalty: 40 cycles
  CPI=2 without any memory stalls (i.e. cache miss not considered)
How we’d proceed?
  Similar to calculating pipeline performance.

## Slide 12: Calculating Cache Performance
Assumption
  Instruction cache miss rate: 2%
  Data cache miss rate: 4% (freq. of load and store: 36%)
  Miss penalty: 40 cycles
  CPI=2 without any memory stalls (i.e. cache miss not considered)
Answer
  Instruction miss cycles: n * 2%*40=0.8n (n: Instruction Count)
  Data miss cycles: 36%*n*4%*40 = 0.58n
  Performance ratio = = = 1.69
  Or, Effective CPI = 2+0.8+0.58=3.38
  (cache miss penalty much higher impact than pipeline hazards.)

## Slide 13: Performance Model
Simplified model: execution time = (execution cycles + stall cycles) ´ cycle time stall cycles = # of instructions ´ miss rate ´ miss penalty
Two ways of improving performance (i.e. to reduce stalls)
  decreasing the miss rate
  decreasing the miss penalty
How can we decrease miss rate?
How can we decrease the miss penalty?
We will introduce a number of basic strategies
  Detailed implementation of these strategies are omitted here
  More strategies discussed in Advanced Computer Architecture

## Slide 14: Improving Cache Performance
Use split caches (i.e. IM and DM have own separate caches) to reduce miss rate because there is more spatial locality in code (one research result shown below)
Decreasing miss rate with set-associativity cache

## Slide 15: Implementation of 4-way Cache
Direct mapped 4-word per block: if one word miss, the whole block needs to be replaced;
4-way: if one word miss then only replace one.
4-way advantage: lower miss rate
4-way disadvantage: more overhead.

## Slide 16: Decreasing Miss Penalty with Multilevel Caches
Add a second level cache:
  often primary cache is on the same chip as the processor
  use SRAMs to add another cache above primary memory (DRAM)
  miss penalty goes down if data is in 2nd level cache
Using multilevel caches:
  try and optimize the hit time on the 1st level cache
  try and optimize the miss rate on the 2nd level cache
  very popular in multicore architecture
  A good topic to study in team project
    Discussion Question: What processor/technology you (your team) choose for the team project? What kind of cache used for that processor?

## Slide 17: Summary
Fast memories are small, large memories are slow
  We really want fast, large memories 
  Caching gives this illusion 
Principle of locality
  Programs use a small part of their memory space frequently
Memory hierarchy
  L1 cache  L2 cache  …  DRAM memory  disk
Memory system design is critical for multicores or multiprocessors