## Slide 1: Lecture 2: Computer Logic
To watch lecture video click link below
Lecture 2 video
To view slides, continue to next slide

## Slide 2: Lecture 2: Computer Logic
Appendix B.1 – B.3

## Slide 3: Introduction
This lecture provides a brief discussion of the basics of logic design
Logic circuits are the fundamental units of computer hardware
Topics covered
  Gates and Truth Tables
  Logic Equations
  Constructing combinational logic circuits

## Slide 4: Truth Table
Signals: asserted or de-asserted
  Asserted: simply called logically true or 1
  De-asserted: simply called logically false or 0
Truth table
  Defines the values of outputs for each possible set of input values
    as seen in CS1300 Discrete Structures
3 inputs => 8 rows
2 inputs => 4 rows

## Slide 5: Logic Equations
Logic Operators
  A + B meaning: A or B
  A o B meaning: A and B (may simply be written as AB)
  meaning: not A (may also be written as ~A,A’
Any set of logic functions can be written as a series of equations
  output on the left-hand side of each equation
  a formula consisting of variables and the above three operators on the right-hand side.
Examples
D = A + B E = C

## Slide 6: Boolean Algebra
Boolean operations follows precedence and associativity rules similar to arithmetic operations, e.g.
Precedence: not (highest), and (next), or (lowest)
Also follows a number of algebraic laws, e.g.
  Identity laws A + 0 = A A o 1 = A
  Commutative law: A + B = B + A A o B = B o A
  …
  (details omitted, please review related topics in CS1300 Discrete Structures )

## Slide 7: Gates
Logic blocks are built from gates that implement basic logic functions
  e.g. an AND gate implements the AND function, and an OR gate implements the OR function.
NOR and NAND gates
  NOR: Inverted OR Gate
  NAND: Inverted AND Gate
XOR gate
  Exclusive OR gate
Gate Drawings

## Slide 8: Gates and Truth Tables
Note: symbols may vary

## Slide 9: Building Combinational Logic Circuits
From Truth Table to Logic Equation
Example 1:
Inputs A and B; output F
A | B | F
0 | 0 | 1
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
A | B | F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Step 1: Find rows where F is 1
Step 2: Write out minimum terms from each row
F = +
Step 3: Write out maximum terms for F
Note: if you’re not familiar with minimum and maximum terms, just ignore these terminology here.

## Slide 10: From truth table to logic equation
Example 2:
Input A, B, C; Output: S, T
S = C + B + A + A B C
A | B | C | S | T
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
T = C + A + A B + A B C
Note: In this class, we will not cover optimization. So just leave the equation unoptimized.

## Slide 11: From logic equation to circuit diagram
F =

## Slide 12
Programming Logic Array (PLA)
Provides a simple solution to building logic circuit

## Slide 13: Decoder
A binary decoder takes n inputs and generates 2n outputs. (e.g. 3 inputs, 8 outputs.)
Each output has a unique bit of 1, the rest all 0s.

## Slide 14: Multiplexor (Mux)
Example: a 2-bit multiplexor where s is the selector.
S | C
0 | A
1 | B
when S = 0, C is the same as A; S = 1, C is B.
A | B | S | C
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Complete truth table
This is the 2-input Mux symbol we will use in this class.

## Slide 15: Summary
Brief introduction to logic design and circuits
  Youtube videos are available for more details
General understanding of computer logic is needed for this class
  However, we will not get into details in this class as we will use block diagrams and description of functionalities to represent hardware units
Study zyBook Appendix B 8.1 – 8.3
Homework H1